## Slide 1
What Works & What Lasts in Farmer-Led Irrigation
Why the Pump is Not the Problem - Building Self - Sustaining Permanent Infrastructure
Eastern and Southern Africa Private Sector Forum on Irrigation
Nairobi, Kenya • October 2026
RESILIENCIA UGANDA LTD
Solar Powered irrigation Solutions
@resilienciaug

## Slide 2
Icebreaker & Key Objectives
SESSION OVERVIEW
"Show of hands: How many have seen a portable, small scale solar pumping kit sitting unused in the field?”
AUDIENCE POLL
1
Contrast 5 years in Uganda with 2.5 years in SE Asia.
Market Realities
2
Examine why the pump kit is only ~25–30% of total system cost.
The True Cost Breakdown
3
Permanent infrastructure with low-cost direct sourcing.
The Resiliencia Model
4
Identify takeaways for affordability, credit, and water access.
Sector Unlocks

## Slide 3
Portable SPIS Kits (~ 800 USD)
Distributed lightweight portable kits on credit & subsidy push.
UGANDA (5 YRS • SOLARNOW)
50% Failure Rate
Within 4 years of mobile operation
Demand: Massive farmer interest in irrigation
Flaw: Credit repayment risks & mis match with site condition
Commercial Sized Systems (~1,200 USD)
Large-scale permanent SPIS on a cash commercial model.
SE ASIA (2.5 YRS • AGROSOLAR)
High Reliability
Dramatically improved asset care & longevity
Model: Commercial cash transactions
Proof: Permanent infrastructure drives farmer ownership
Learnings & Market Realities
FIELD EXPERIENCE & EVIDENCE

## Slide 4
1. Solar Pump Package - ~10,000 liter / day
2.0M UGX (40% of 5M base)
2. Av. Transport & Installation Service
1.0M UGX (20% of 5M base)
3. Water Distribution, Cables & Protection
2.0M UGX (40% of 5M base)
+ Overhead Tank & Tank Stand
+5.0M UGX
+ Shallow Well Digging (Water Source)
+5.0M UGX
Standard System Quote Ratio Breakdown
Core Insight
The pump itself is just ~20% of total investment.
Water access, distribution and storage are the real cost items.
The Pump is NOT the Problem
FINANCIAL ANALYSIS OF A QUOTE
SESSION OVERVIEW

## Slide 5
Our Model is Build on Affordability & System Longevity
THE RESILIENCIA MODEL
Customized & Integrated Farm Infrastructure
Infrastructure as the Anchor
Long-term civil and piping infrastructure stays fixed on the farm. The solar pump is treated as an easily replaceable component.
Ultra-Lean Sales Operations
Eliminating heavy retail branch networks keeps distribution hyper-efficient and retail prices at rock bottom.
Direct Factory Sourcing
Sourcing pumps directly from Tier-1 manufacturers in China minimizes unit cost, making pump replacement cheap and simple.

## Slide 6
UNLOCK 01
Commercial Affordability
Move away from subsidy-led market distortions. Unlock commercial asset finance and direct sourcing to make hardware genuinely self-sustaining.
UNLOCK 01
Permanent Infrastructure
Assist farmers in co-financing long-term civil works, trenching, and water distribution networks that outlast individual pump units.
UNLOCK 02
Access to Water
Direct public and donor support toward water source development (shallow wells, hydrology testing, drilling) rather than subsidizing pumps.
What the Sector Needs to Unlock
SECTOR RECOMMENDATIONS

## Slide 7
sandra@resiliencebv.com
+256749629925
Sandra Bos
KEY TAKEAWAY
Thank You
By combining permanent water distribution infrastructure, direct-sourced modular hardware, and lean distribution, SPIS can become affordable and financially self-sustaining.
Remaining Sector Challenge: Access to Water
@resilienciaug